### Data Range by Station

### Station Name	Station ID	City	GPS Coordinates	Available Data

### Ft. Meade	FMEMD	Ft. Meade	39.11, -76.72	7/1998 – 9/2004

### Beltsville	BLTMD	Beltsville	39.06, -76.88	5/2005 - Present

### Piney Run	PNRMD	Frostburg	39.71, -79.01	5/2005 – Present

### Horn Point	HPLMD	Cambridge	39.59, -76.14	4/2012 – Present

### Contact Information

### Laura Warren	Michael Woodman

### Meteorologist IV / Senior Scientist	Chief of Air Quality Measurements, Modeling, and

### Modeling, & Analysis Division

### ARMA / Air Monitoring Program	ARMA / Air Monitoring Program

### Phone: 410-537-3122	Phone: 410-537-3229

### Email: laura.warren@maryland.gov	Email: michael.woodman@maryland.gov

### Format of Wind Data Files

*.cns: Wind data from each consensus average are appended to text file(s) with the name wYYDDD.cns where w for winds, YY is the 2-digit year, and DDD is the day-of-year. Prior to 4/2012, the “consensus average” was a 15-minute average reported every 15 minutes. After 4/2012, the “consensus average” is a 30-minute average reported every 6 minutes. The format of a wind consensus record is listed in Table 1.

*.asd: Prior to 4/2012, see *.cns description. The name is wYYYY-MM-DD_HH-00.asd where w is for winds, YYYY is the 4-digit year, MM is the month, DD is the day, and HH is the hour in UTC. After 4/2012, see README_ASD.pdf for file format.

### Format of Virtual Temperature Data Files

*.cns: Radio acoustic sounding system (RASS) virtual temperature data from each consensus average are appended to text file(s) with the name tYYDDD.cns where t for temperature, YY is the 2-digit year, and DDD is the day-of-year. The format of a single RASS record is listed in Table 2.

*.asd: Prior to 4/2012, see *.cns description. The name tYYYY-MM-DD_HH-00.asd where t is for temperature, YYYY is the 4-digit year, MM is the month, DD is the day, and HH is the hour in UTC. After 4/2012, see README_ASD.pdf for file format.

Table 1. The format of a wind record for *.cns files and, prior to 4/2012, for *.asd files.

(Adapted from Louisiana Universities Marine Consortium)

| Line # | Description |
| --- | --- |
| Line 1 | Station name (as many as 28 characters) |
| Line 2 | "WINDS rev 5.0" (rev number will change if file format changes) |
| Line 3 | N Latitude, W Longitude, and site elevation (m) |
| Line 4 | Date and begin time of consensus: yy mm dd hh mn ss plus # minutes to add to get UTC. (BEGIN TIME OF AVERAGING TIME INTREVAL!!! K.V.) |
| Line 5 | Consensus averaging time (minutes); number of beams; number of range gates |
| Line 6 | For each beam, number of records required to make consensus (num); total number of records (tot); consensus window size (m/s); in the format: num:tot (window) |
| Line 7 | No. of coded cells, no. of spectra, pulse width (ns), and inter-pulse period (µs), each with a pair of values: first value is for oblique beams, second for vertical |
| Line 8 | Full scale Doppler velocity (m/s), oblique and vertical; Vertical correction applied to oblique beams? (0 = no, 1 = yes); Delay to first gate (ns), oblique and vertical; Number of gates, oblique and vertical; Spacing of gates (ns), oblique and vertical |
| Line 9 | Azimuth and elevation of each beam (9s indicate vertical beam not used). NOTE: All *.asd and *.cns files for Beltsville and Piney Run prior to 4/2012 mislabel beam direction order. Beams listed as Vertical, West, North, East, South. Actual order is Vertical, North, East, South, West. MDE does NOT operate a vertical beam at the profilers (except for Ft Meade), thus vertical is derived using oblique beams. |
| Line 10 | Labels for columns that follow |
| Line 11 etc | Height above ground (km); Wind speed and direction (m/s and deg E of N from N, 9s indicate did not reach consensus); (Optional) U,V,W velocities; (Optional) QC flag for wind speed and direction; Radial velocities for each beam (m/s) in order given in azimuth and elevation line (positive toward radar; 9s indicate vertical beam not used - NOTE: MDE does not operate a vertical beam but derives vertical radial velocity which is negative vertical velocity, -W); Number of records that made consensus (in same order); Average signal to noise ratio (SNR, dB) of records in consensus (same order); (Optional) QC flag for each radial velocity |
| Last line | A single ‘$’ character |

Table 2. The format of RASS, or Tv, record for *.cns and, prior to 4/2012, for *.asd files.

(Adapted from Louisiana Universities Marine Consortium)

| Line # | Description |
| --- | --- |
| Line 1 | Station name |
| Line 2 | "RASS rev 5.0" (rev number will change if file format changes) |
| Line 3 | N latitude, W longitude, and site elevation (m) |
| Line 4 | Date and begin time of consensus: yy mm dd hh mn ss plus # minutes to add to get UTC |
| Line 5 | Consensus averaging time (minutes; number of beams; number of range gates) |
| Line 6 | Number of records required to make consensus (num); total number of records (tot); and the consensus window size (m/s); in the format: num:tot (window) |
| Line 7 | no. of coded cells, no. of spec, pulse width (ns), and inter-pulse period (µs) |
| Line 8 | Full scale Doppler value (m/s); Delay to first gate (ns); Number of gates; Spacing of gates (ns) |
| Line 9 | Azimuth and elevation.(9s indicate vertical beam not used) |
| Line 10 | Labels for columns that follow |
| Line 11 etc | Height above ground (km); Uncorrected virtual temperature consensus (deg C); Corrected virtual temperature consensus (deg C); Vertical wind consensus (9s indicate vertical beam not used, w-component, positive upward, m/s); Number of records that made consensus (for the 3 values in same order); Average signal to noise ratio (SNR, dB) of records in consensus (same order); (Optional) QC flag for T, Tc, and W |
| Last line | A single ‘$’ character |