## Slide 1: AOSC 634/458R Air Sampling and Analysis
Lecture 2
Measurement Theory
Performance Characteristics of instruments
Dynamic Performance of Sensor Systems
Response of a first order system to
A step change
A ramp change
Copyright Brock et al. 1984; Dickerson 2015

## Slide 2: Dynamic Response Sensor output in response to changing input.
Time response: First Order Systems
For a step change in input:
X’(t’) = 1 – e–t’
Where X’ is the normalized output (0-1).
t’ is the time in system time constants, i.e.,
t’ = t/t where t is the e-folding time constant.
95% of a step change occurs in 3t’.

## Slide 3: Response of a first order system to a step increase of input.

## Slide 5: The finite response time of a first order system creates a time lag for the output relative to the input. For a step change of duration much longer than the time constant of the system: Where tmo is the time of the mid point of the maximum output. If t’ >> 1, then t’mi ≅ t’mo – (2t’)
Signal
Time
| | | |
t’0 t’mi t’mo t’f
Input
output
0 1
| |

## Slide 7: RF2: Morning Vertical Profile over New Haven & over the Sound

## Slide 8
Chart: Beltsville CO and NOy Vertical Profiles (110721, 11:24-11:29 EST) Whole Profile

## Slide 9: Time Lag, continued.
The apparent middle of the step, a pollution plume or warm air parcel perhaps, will appear about 2t’ later than it occurred. In a sounding or aircraft spiral this shows up as an difference in altitude for instruments with different response times.
The time integral of the input and output will, however, be the same.

## Slide 10: Time Lag, continued.
This holds even if t < t’ although the amplitude will be in error (too small).

## Slide 11: For a step change of duration less than the response time of the instrument (t’ or t) the integral is still the same as the input integral, but the amplitude is now reduced. At very high frequencies (>> 1/t), the input begins to look like a DC signal again.
Signal
Time
Input
output
0 1
| |

## Slide 12: Response to a ramp input.
Or in normalized variables
For all t’ > 0
The transient approaches zero after a few time constants.
For t >> t’

## Slide 13: Response of a first order system to ramp input in normalized variables. In Brock’s book X’(t’) is output, the same as X’O(t’)
The output is always less than the input by a constant.
The output lags the input amplitude by t’.
Output
Input

## Slide 14: If time t is less than a few time constants t then the output Xo is a function of time given by Where the far right term is transient.

## Slide 15: Implications
A first order system is a crude low-pass filter. For t’ > 10 a strong attenuation occurs.
Example: Spring – shock absorber (dashpot) system.
R

## Slide 16: Implications, continued.
Example: Spring – shock absorber (dashpot) system.
R
Restoring force Fspring = -kX
Resistive force of Fshock = -R (dx/dt)
(For gas shocks remember Dp a F)
Fspring lags displacement by p (180o)
Fshock lags displacement by p/2 (90o)
Fsp + Fsh + FI = 0

## Slide 17: Implications, continued.
For low frequency input (a << 1, or long slow bumps):
Fsh ~ 0 and Fsp is large
For high frequency input (a >>1, or closely space bumps):
FI(t) leads displacement by p/2
Fsh is large (dx/dt is large)
The shock absorber prevents the car from bouncing when it goes over a big bump.
If the displacement is small the Fsp is small.

## Slide 18: Summary
Many environmental sensors demonstrate first order response characteristics.
The time constant, t, of a first order system can be determined from the response to a step decrease:
ln(X0/Xt) = t/t
t = t/(ln(X0/Xt))
The finite response time of a sensor not only dictates the sampling time necessary to respond to a step change, it also:
Creates a time lag between an observed signal and its observation.
Induces an amplitude depression for high frequency fluctuations.

## Slide 19: Summary
As an example, fires produce both black carbon and CO2, but think of correlating the slow response Aethalometer with the fast response Picarro. You need to know the first order response time t for each instrument. Correlating bumps or spikes requires adjusting for both lag and amplitude. This is in addition to any lag caused by different transport times between inlet and detector.

## Slide 20: Next Time
The time response, X, of a first order system can be described by a linear first order ODE.